## Slide 1: Intro to Petrographic Microscopes B
EPSS 51
Adapted from Greg Druschel, University of Delaware

## Slide 2: The Petrographic Microscope
Ocular
Analyzer (upper polar)
Lower polar
Rotating stage
Gypsum plate
Rotating nosepiece
(use to change objectives!)
Objectives (do not touch!)
Arm
Condenser
Light source
Focus
Bertrand lens (inverts light)
Notes: http://www.microscope.com/media/catalog/product/cache/2/image/9df78eab33525d08d6e5fb8d27136e95/o/m/om239p__3_of_5_copy.png

## Slide 3
2) Insert the analyzer (upper polarizer)
west (left)
east (right)
Now what happens?
What reaches your eye?
Why would anyone design a microscope that prevents light from reaching your eye???
XPL=crossed polars
south (front)
north (back)
Black!! (“extinct”)

## Slide 4
3) Now insert a thin section of a rock
west (left)
east (right)
Light vibrating E-W
How does this work??
Unpolarized light
Light vibrating in many planes and with many wavelengths
Light and colors reach eye!

## Slide 5
Conclusion has to be that minerals somehow reorient the planes in which light is vibrating; some light passes through the upper polarizer

## Slide 6
4) Note the rotating stage
Most mineral grains change color as the stage is rotated; these grains go black 4 times in 360° rotation- exactly every 90o
Glass and a few minerals stay black in all orientations:
These minerals are anisotropic
These minerals are isotropic

## Slide 7
Some generalizations and vocabulary
All isometric minerals (e.g., garnet) are isotropic – they cannot reorient light. Light does not get rotated or split; propagates with same velocity in all directions
  These minerals are always black in crossed polars.
All other minerals are anisotropic – they are all capable of reorienting light (transmit light under cross polars).
All anisotropic minerals contain one or two special directions that do not reorient light.
  Minerals with one special direction are called uniaxial
  Minerals with two special directions are called biaxial

## Slide 8
Isotropic
Uniaxial
Biaxial
How light behaves depends on crystal structure
Isometric
  All crystallographic axes are equal
Orthorhombic, monoclinic, triclinic
  All axes are unequal
Hexagonal, tetragonal
  All axes  c are equal but c is unique

## Slide 9
Isotropic minerals: light does not get rotated or split; propagates with same velocity in all directions
Anisotropic minerals:
    Uniaxial - light entering in all but one special direction is resolved into 2 plane polarized components that vibrate perpendicular to one another and travel with different speeds
    Biaxial - light entering in all but two special directions is resolved into 2 plane polarized components…
  Along the special directions (“optic axes”), the mineral thinks that it is isotropic - i.e., no splitting occurs
  Uniaxial and biaxial minerals can be further subdivided into optically positive and optically negative, depending on orientation of fast and slow rays relative to xtl axes

## Slide 10: ‘Splitting’ of light  what does it mean?
For some exceptionally clear minerals where we can see this is hand sample this is double refraction  calcite displays this
Light is split into 2 rays, one traveling at a different speed, and this difference is a function of thickness and orientation of the crystal
ALL anisotropic minerals have this property, and we can ‘see’ that in thin sections with polarized light!

## Slide 11: Anisotropic crystals
O E
Fig 6-7 Bloss, Optical Crystallography, MSA
Calcite experiment and double refraction
O-ray (Ordinary)  ω
Obeys Snell's Law and goes straight
Vibrates ^ plane containing ray and c-axis (“optic axis”)
E-ray (Extraordinary)  ε
deflected
Vibrates in plane containing ray and c-axis

## Slide 12
O E
Fig 6-7 Bloss, Optical Crystallography, MSA
IMPORTANT: A given ray of incoming light is restricted to only 2 (mutually perpendicular) vibration directions once it enters an anisotropic crystal
Called privileged directions
Each ray has a different n
  w = no
  e = nE
  in the case of calcite w < e
…which makes the O-ray dot appear above E-ray dot
Different rays going different speeds means they are at different wavelengths

## Slide 13
If I slow down 1 ray and then recombine it with another ray that is still going faster, what happens??

## Slide 14: Difference between our 2 rays
Apparent birefringence – d – difference in refractive index (speed) between the 2 rays
Retardation – D  distance separating the 2 rays (nm)
d = thickness of medium
Retardation therefore is a function of the apparent birefringence and the thickness of the crystal
  ideally all thin sections are 0.3 mm, but mistakes do happen…

## Slide 15
Polarized light going into the crystal splits into two rays, going at different velocities and therefore at different wavelengths (colors)
one is O-ray with n = w
other is E-ray with n = e
When the rays exit the crystal they recombine
When rays of different wavelength
combine  what things happen?
e
w
polarizer

## Slide 17
  1) Find the crystal of interest showing the highest colors (D depends on orientation)
  2) Go to color chart
    thickness = 30 microns
    use 30 micron line + color, follow radial line through intersection to margin & read birefringence
Estimating birefringence

## Slide 18
Example: Quartz w = 1.544 e = 1.553
w
e
1.553
1.544
Data from Deer et al
Rock Forming Minerals
John Wiley & Sons

## Slide 19
Sign??
(+) because e > w
  e - w = 0.009 called the birefringence (d) = maximum interference color (when seen?)
  What color is this?? Use your chart.
Example: Quartz w = 1.544 e = 1.553

## Slide 20
What interference color is this?

## Slide 21
Colors one observes when polars are crossed (XPL)
Color can be quantified numerically: d = nhigh - nlow

## Slide 22: Rotation of crystal?
Retardation also affected by mineral orientation!
As you rotate a crystal, observed birefringence colors change
Find maximum interference color for each in practice

## Slide 23: Extinction
When you rotate the stage  extinction relative to the cleavage or principle direction of elongation is extinction angle
Maximum interference color  ∆𝛼  extinction angle